## Slide 1: PIC18F4520 Assembly Language Programming (II)
Instruction Set (Logic and Branch)
Yu-Syuan Liu
劉宇軒

## Slide 2
LAB
  Lab3-1:
    Implement two logic operations: 1. NAND 2. NOR
  Lab3-2:
    Practice Logical Instructions and Control Operations step by step.
  Bonus:
    Explain one instruction of four categories to TAs.
Outline

## Slide 3: LAB - Lab3-1
Lab3-1
Recall what you had learned in Digital Logic Design (數位邏輯設計) class. (If you have already forgot all thing, Google is always your best friend.)
Implement two logic operations below:
  1. NAND: 01011101 NAND 01111000, and store result in LATD
  2. NOR: 10010110 NOR 01101001, and store result in LATC
Tips:
  Use WREG as your temporary register.
  Use AND, OR, XOR instructions to finish ONLY.
  (DO NOT give the LATD and LATC values DIRECTLY)

## Slide 4: LAB - Lab3-2
Lab3-2
Practice following Logical Instructions and Control Operations step by step.
1. Add from 1, 2, … to XX, and store in LATA.
  Tips:
  a. Use WREG as a incrementally temporary register.
  b. ADDWF is a good instruction for sum of two registers.
  c. If there are nothing change about Overflow Bit in STATUS register, Branch back and do this sum loop.
  d. Use above Control Operation and see the result, what happen? And what is the value of XX finally?

## Slide 5: LAB - Lab3-2
2. After finishing the summation, use GOTO to the label named Rotate. And label Rotate must under these:
  NOP
  NOP
  NOP
  GOTO Initial
3. Give value 0xBF to your LATB register, and do any one of following two options:
  Option A: Rotate Left and store in WREG, C = 1, what is result?
  Option B: Rotate Right and store in WREG, C = 1, what is result?
  Take Care about your STATUS register.

## Slide 6: LAB - Lab3-2
Flow Diagram:
Adding loop in LATA
NO
YES (when XX = ?)
GOTO Rotate Label
( Must jump over the NOP and GOTO instr. )
Give 0xBF to LATB
WREG = ??
Carry = 1
WREG = ??
Carry = 1
Option A.
Option B.
In C code:
for(WREG = 0; OV != 1; WREG++){
LATA += WREG;
}
Label Rotate:
OverFlow Bit change?

## Slide 7: LAB - Lab3-2
Flow Diagram:
Adding loop in LATA
NO
YES (when XX = ?)
GOTO Rotate Label
( Must jump over the NOP and GOTO instr. )
Give 0xBF to LATB
WREG = ??
Carry = 1
WREG = ??
Carry = 1
Option A.
Option B.
In C code:
for(WREG = 0; OV != 1; WREG++){
LATA += WREG;
}
Label Rotate:
OverFlow Bit change?
1.

## Slide 8: LAB - Lab3-2
Flow Diagram:
Adding loop in LATA
NO
YES (when XX = ?)
GOTO Rotate Label
( Must jump over the NOP and GOTO instr. )
Give 0xBF to LATB
WREG = ??
Carry = 1
WREG = ??
Carry = 1
Option A.
Option B.
In C code:
for(WREG = 0; OV != 1; WREG++){
LATA += WREG;
}
Label Rotate:
OverFlow Bit change?
2.

## Slide 9: LAB - Lab3-2
Flow Diagram:
Adding loop in LATA
NO
YES (when XX = ?)
GOTO Rotate Label
( Must jump over the NOP and GOTO instr. )
Give 0xBF to LATB
WREG = ??
Carry = 1
WREG = ??
Carry = 1
Option A.
Option B.
In C code:
for(WREG = 0; OV != 1; WREG++){
LATA += WREG;
}
Label Rotate:
OverFlow Bit change?
3.

## Slide 10: LAB - Bonus
Read four instructions of the four basic categories and explain to TA. (Instr. is selected by TA)
1. Open the PIC18FXXXX Data Sheet website and find out the instruction by your own hands.
2. Explain each step of spec. as clearly as possible.
3. You can do this Bonus ONLY after you finish two Labs above (Lab3-1 and Lab3-2).

## Slide 11: LAB – Bonus (cont.)

## Slide 12: LAB – Bonus (cont.)
Choice 1.
BYTE-ORIENTED OPERATIONS - ADDWF
Choice 2.
BIT-ORIENTED OPERATIONS - BCF
Choice 3.
CONTROL OPERATIONS – BC
Choice 4.
LITERAL OPERATIONS - MOVWF

## Slide 13
Thanks you for listening